## Slide 1: CoolMOS™ SSR – Demonstrator for in-circuit evaluation – Version 1
Input | +5 V / 5 .. 20 mA | diode-like input, external current limitation necessary
Output | 250 VAC / 2 A | Resistive / capacitive load tested (X=15)
RDSon | 44 mΩ / 80 mΩ | Total resistance
Isolation | 600 VRMS basic | Contact 1 – Contact 2 Input - Output
Temperature | 0°C .. 75°C | Limited by Gate driver
Dimensions | 15 x 21 x 6 mm | h x w x d
Prototypes will be provided as coated PCBs w/o 2nd level packaging (housing).
Constructed space
PCB footprint